Technical Data Sheet

| Revision Date | 24 May 2018 |
| --- | --- |
| Multisorb Part Number | Product Name | Description |
| 02-00397DG04 | Dri-Can® Desiccating Containers | Dri-Can® Indicating Silica Gel |

MATERIALS OF CONSTRUCTION

| Components | Indicating Silica Gel Bead | Aluminum Dri-Can® |
| --- | --- | --- |

PHYSICAL ATTRIBUTES

| Attribute | Specification | Comments |
| --- | --- | --- |
| Sorbent Weight | 40 Grams ( 4 Grams | N/A |
| Length | 4.060” ( 0.060” | 103.12mm ( 1.52mm |
| Width | 2.150” ( 0.060” | 54.61mm ( 1.52mm |
| Thickness (at time of manufacture) | 0.575” ( 0.060” | 14.61mm ( 1.52mm |
| Moisture Content | 5.0% Maximum | Product is quality released using residual moisture testing per Multisorb Loss on Drying Test Method (10-20 grams at 150°C ( 15°C for 3 hours Minimum). |
| Printing | Metal Stamped | Company Name |

PACKAGING, LABELING, PRODUCT STORAGE, AND WARRANTY PERIOD

| Attribute | Specification |
| --- | --- |
| Quantity | 1 part per foil barrier. Pack 24 pouches per carton. Total: 24 parts. |
| Labeling | Manufacturer’s CAUTION statement printed on the carton. |
|  | Manufacturer's name, Description of desiccant, Quantity per container, Manufacturer's part number, Manufacturer's control number. |
| Product Storage | Recommended storage in a non-condensing environment. Avoid temperatures above 90ºF (32ºC). |
| Warranty Period | Product meets specified physical attributes for a period of 1 year from date of manufacture when stored in original unopened packaging. |

# Text boxes

EXCEPT TO THE EXTENT REQUIRED BY STATE LAW, SELLER EXPRESSLY DISCLAIMS ALL WARRANTIES, EXPRESSED OR IMPLIED, INCLUDING ANY IMPLIED WARRANTY OF MERCHANTABILITY OR FITNESS FOR A PARTICULAR PURPOSE.

EXCEPT TO THE EXTENT REQUIRED BY STATE LAW, SELLER EXPRESSLY DISCLAIMS ALL WARRANTIES, EXPRESSED OR IMPLIED, INCLUDING ANY IMPLIED WARRANTY OF MERCHANTABILITY OR FITNESS FOR A PARTICULAR PURPOSE.